## Slide 1: Worship Space
Decorations and acoustics
Steve Elzinga

## Slide 2: The physical space where you worship can be decorated to enhance the worship experience
Common Church Vision:
To walk with God,
to walk with God’s people,
and to share our God walk with those who do not have a walk with God.

## Slide 3
Decorations:
Banners
Paintings
Floral
PowerPoint
Sculptures
Pottery
Carpet
Wall paint
Words on walls
Drapery
Creative stuff

## Slide 4
Art vs. Craft
Craft is generally just decoration we think looks good
Art has meaning, often multiple meanings, and sometimes hidden meaning

## Slide 5
The acoustics of the space
Nothing affects sound more than the space where the worship takes place
Library vs. bathroom
Things that affect the sound:
  Carpet vs. hard floors
  People vs. empty
  Flat wall vs. stuff on the wall
  High ceiling vs. Low ceiling
  Ceiling tiles vs. hard surface
  Speakers in ceiling or on the floor

## Slide 6
Analyze your sound space, if possible
Buy a 32 band EQ and push each band up and see which ones give the most unwanted feedback and then back those specific bands down
Download some room-analyzing software and a special neutral mic to do some testing

## Slide 7
Five common problems and what to do about your space and acoustics
Low ceiling, dead space
    Try taking the ceiling tiles out to liven things up a bit
    Add more reverb to the mix
    Get rid of the carpet
    Get hard backed chairs instead of cushioned
High ceilings, too alive space
  Build 2 foot by 4 foot fames covered with cloth and backed with acoustical deadening material

## Slide 8
Five common problems and what to do about your space and acoustics
Slap back off the back wall. Music doesn’t sound clear. The pastor’s voice has a bit of an echo
    Build 2 foot by 4 foot fames covered with cloth and backed with acoustical deadening material
  A lot of feedback problems
    Get a 32 band EQ and try to illuminate the problem frequencies
    Make sure worship team is behind the main speakers

## Slide 9
Five common problems and what to do about your space and acoustics
People don’t like to sing because all they can hear is their own voice
    Put reflection panels in ceiling slanted away from the stage